## Slide 1: Device Model Summary Model ID = dtmi:com:Microchip:PIC32CMLS60_Curiosity;1 File Name = PIC32CMLS60_curiosity-1.json
Type | Name | Schema | Example JSON Message/Format
Telemetry | potentiometer | integer | {“potentiometer”:4096}
Telemetry | button_event | Object | {“button_event”:{“button_name”:“BTN”,“press_count”:7}}
Property (Writable) | LED0 | LedState | {“LED0”:{“ac”:200,“av”:1024,“ad”:“success”,“value”:1}}
Property (Writable) | LED1 | LedState | {“LED1”:{“ac”:200,“av”:576,“ad”:“confirmed”,“value”:2}}
Property (Writable) | telemetryInterval | integer | {“telemetryInterval”:{“ac”:200,“av”:3901227608, “ad”:“OK”,“value”:10}}
Command (Request) | reboot | Object | {“delay”:“PT5S”}
Command (Response) | reboot | Object | {“status”:“success”,“delay”:5}
Command (Request) | recvMsg | Object | {“recvMsgString”:“Hello World!!!”}
Command (Response) | recvMsg | Object | {“status": "received”}